## Slide 1: MemcachedGPU Scaling-up Scale-out Key-value Stores
Tayler Hetherington – The University of British Columbia
Mike O’Connor – NVIDIA / UT Austin
Tor M. Aamodt – The University of British Columbia

## Slide 2: Problem & Motivation
Data centers consume significant amounts of power
http://crimsonrain.org/hawaii/images/9/9c/Google-datacenter_2.jpg

## Slide 3: Problem & Motivation
Data centers consume significant amounts of power
Continuously growing demand for higher performance
Horizontal or vertical scaling
  GP-GPUs

## Slide 4: Why GPUs?
Highly parallel
High energy-efficiency
  Green500: GPUs in 7 of top 10 most energy-efficient super computers
General-purpose & programmable
CPU
GPU

## Slide 5: Highlights
Network and Memcached processing on GPUs
10 GbE line-rate at all request sizes
95% latency < 300 us @ 75% peak throughput
75% energy-efficiency of FPGA
Maintain Memcached QoS with other workloads

## Slide 6: GPU Network Offload Manager (GNoM)
Packet metadata
Network Card
CPU
Kernel Module & Network Driver
OS
Pre-processing
Post-processing
User-level
Networking
Application
GPU
Packet data
Response & Recycle
Receive
Send

## Slide 7: Challenges | Networking on GPUs
High throughput
  Efficient data movement
  Request-level parallelism through batching
Low latency
  Small batches
  Multiple concurrent batches
  Task-level parallelism

## Slide 8: Application | Memcached
Web Tier
Memcached
Distributed Key-value Store
Storage Tier
GET
SET

## Slide 9: Challenges | MemcachedGPU
Limited GPU memory sizes
Key & Value Storage
Hash Table
CPU Memory
GPU Memory
CPU Memory
Hash Table + Key storage
Value Storage

## Slide 10: Challenges | MemcachedGPU
Dynamic memory allocation
  Dynamic hash chaining
Reduce GET serialization
Hash Table
  Static set-associative
Set 0
Set 1
Set N

## Slide 11: Experimental Methodology
Single client-server setup with 10 GbE NIC
High-performance NVIDIA Tesla K20c GPU
  Kepler | TDP = 225W | # Cores = 2496 |Cost = $2700
Low-power NVIDIA GTX 750 Ti GPU
  Maxwell | TDP = 60W | # Cores = 640 | Cost = $150

## Slide 12: Evaluation| Throughput
Chart: Key Size (Bytes)
| 16.0 | 32.0 | 64.0 | 128.0
High-performance GPU | 9.92 | 9.98 | 9.98 | 10
Low-power GPU | 9.87 | 9.91 | 10 | 10

## Slide 13: Evaluation| Latency

## Slide 14: Evaluation| Power
Chart: Average MRPS
| 2.19 | 3.96 | 5.76 | 7.58 | 10.1 | 12.8
Full System Power | 163.7114 | 169.9 | 174.7308 | 177.9348 | 203.4143 | 208.5793
High-performance GPU Power | 56.6 | 60 | 63.03 | 65.6 | 67.7 | 70.44
High-performance GPU 225W TDP

## Slide 15: Evaluation| Energy-efficiency

## Slide 16: Evaluation| Workload Consolidation
Limited multiprogramming on current GPUs
GPU
Low-priority background task
Memcached
Blocked

## Slide 17: Evaluation| Workload Consolidation
18X maximum request latency
50% low-priority background runtime
Background task running

## Slide 18: Conclusions
Network and Memcached processing on GPUs
10 GbE line-rate at all request sizes
95% latency < 300 uS @ 75% peak throughput
75% energy-efficiency of FPGA
Maintain Memcached QoS with other workloads
Code: https://github.com/tayler-hetherington/MemcachedGPU