## Slide 1: LossRadar: Fast Detection of Lost Packets in Data Centers
Yuliang Li
Rui Miao Changhoon Kim Minlan Yu
Notes: Give: What I am doing
Emphasize name
==
2 options:
1. highlight loss is the top issue in dc
2. do not say here, say after well motivated
==
Need better visibility
Problems: packet loss, transient loops, blackholes
DC larger -> problems more frequently and difficult
So we need better tools that can provide better vis.
Joint work between …
Data center networks need better visibility. There are many problems that have not been well handled such as packet loss, transient loops and blackholes. And as the data centers are growing larger, these problems happen more frequently and becomes more difficult to detect. So we need better tool that can provide better visibility.

## Slide 2: Packet loss diagnosis is important
Losses are common because of the large scale
  40-80 machines see 50% packet loss [Jeff Dean’s talk from Google]
  Network maintenance jobs cause 30-minute random connectivity losses [Jeff Dean’s talk from Google]
  One to ten new switch blackholes every day [Microsoft]
Losses have high impact
  High latency, low throughput
  Break connection
Notes: Citations:
Packet loss is common, not diagnosis is common
keep sentences short
The speaking for The second evidence
===
Title change (critical, etc.): detecting..
Give a percentage of 40-80

## Slide 3
I fail to connect!
Me too!
Counters
Where?
Hard to locate
Not generic
Problems:
Notes: Today’s commodity switches do not expose much information. The most useful one is … But they are not generic [click], because many problems …

## Slide 4
4
Traceroute
Where?
x 10,000s
Hard to locate
Not generic
Problems:
Notes: What kind of large overhead

## Slide 5
5
Where?
S1
S2
S3
S4
S5
S6
…
…
…
Large overhead
Hard to locate
Not generic
Problems:

## Slide 6
6
Why?
Where?
Large overhead
Hard to locate
Not generic
Problems:
Unknown root cause
Time consuming
Congestion?
Blackhole?
Random drops?
    Detect losses
    Fast
    With location info.
    Generic to all types of losses
    Low overhead
    Diagnose losses
    Root causes
Notes: After so many troubles, …
Explain random drops (e.g. link flapping)

## Slide 7: Challenge: diversity of loss types
OutputPort 1
Output Port n
Input Port 1
Input Port n
Input buffer
…
parser
Ingress match-actions
(L2->L3->ACL)
Shared buffer
Egress match-actions
…
Switch CPU
Configure
Rule
corruptions
mis-config
updates
Resource shortage
Resource shortage
Packet corruptions
Grey failure
Rule corruptions
mis-config
updates
Takeaway:
Need to be generic to all types
Notes: Happen at diff stages by diff reasons
First talk about all stages
each stages
talk about some (2) examples, and pop up the rest
====
Speed up
[solved] do not make packet cover the texts
maybe highlight boxes
==
Write clearly : rule corruption, packet corruption
Make figure wider
different corruption
===
Think about the order of 3 challenges
===
Introduce pipeline
However, many possible reasons
Hard for vendors to
Takeaway, … cover any types of losses.
put location challenge before

## Slide 8: Challenge: diversity of loss types
OutputPort 1
Output Port n
Input Port 1
Input Port n
Input buffer
…
parser
Ingress match-actions
(L2->L3->ACL)
Shared buffer
Egress match-actions
…
Switch CPU
Configure
Rule
corruptions
mis-config
updates
Resource shortage
Resource shortage
Packet corruptions
Grey failure
Rule corruptions
mis-config
updates
Takeaway:
Need to be generic to all types
Notes: Happen at diff stages by diff reasons
First talk about all stages
each stages
talk about some (2) examples, and pop up the rest
====
Speed up
[solved] do not make packet cover the texts
maybe highlight boxes
==
Write clearly : rule corruption, packet corruption
Make figure wider
different corruption
===
Think about the order of 3 challenges
===
Introduce pipeline
However, many possible reasons
Hard for vendors to
Takeaway, … cover any types of losses.
put location challenge before

## Slide 9: Challenge: diagnose root causes
Chart: Time (us)
| 1.0 | 2.0 | 3.0 | 4.0 | 5.0 | 6.0 | 7.0 | 8.0 | 9.0 | 10.0 | 11.0 | 12.0 | 13.0 | 14.0 | 15.0 | 16.0 | 17.0 | 18.0 | 19.0 | 20.0 | 21.0 | 22.0 | 23.0 | 24.0 | 25.0 | 26.0 | 27.0 | 28.0 | 29.0 | 30.0
Y-Value 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 1 | 0 | 0 | 1 | 0 | 1 | 1 | 0 | 1 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Chart: Time (us)
| 1.0 | 2.0 | 3.0 | 4.0 | 5.0 | 6.0 | 7.0 | 8.0 | 9.0 | 10.0 | 11.0 | 12.0 | 13.0 | 14.0 | 15.0 | 16.0 | 17.0 | 18.0 | 19.0 | 20.0 | 21.0 | 22.0 | 23.0 | 24.0 | 25.0 | 26.0 | 27.0 | 28.0 | 29.0 | 30.0
Y-Value 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1
Chart: Time (us)
| 1.0 | 2.0 | 3.0 | 4.0 | 5.0 | 6.0 | 7.0 | 8.0 | 9.0 | 10.0 | 11.0 | 12.0 | 13.0 | 14.0 | 15.0 | 16.0 | 17.0 | 18.0 | 19.0 | 20.0 | 21.0 | 22.0 | 23.0 | 24.0 | 25.0 | 26.0 | 27.0 | 28.0 | 29.0 | 30.0
Y-Value 1 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 1 | 1
congestion
blackhole
Random drop
Takeaway:
Need the information of individual losses
Notes: Relate diff types to diff root cause
==
[solved] make title more clear: pattern, etc.

## Slide 10: LossRadar overview
Knowing location  Install meters to monitor traffic
Fast detection  Frequently send traffic digest to collector
Being generic  Compare packets across hops
Need info of individual losses  Include details of each loss
Low overhead ?
Digest Collector
Traffic Digest
Traffic Digest
Traffic Digest
Notes: Change Overview
[solved] order of points
==
Add low overhead
Give key insight after
===
Our goal is to build a system that …
So we install meters in the network, so know locations
Each meter generates digest based on the pkts it sees, and periodically .. -> fast
Also include details of packets in the digest
Finally, collector detect loss by compare the set of pkts at two meters, and the diffs are the losses.
1st chanllenge: How to choose the locations to install meters, --> whole network

## Slide 11: Storing all packets is too heavy
Collector
Switches

## Slide 12: Storing all packets is too heavy
Capture: O(#loss)
Memory: O(#packet)
= 10-5~10-4
Collector
Switches
Notes: Leave 2 seconds for reader to think
with concrete numbers, instead of ratios

## Slide 13: Solution: put all packets in a small memory
View the problem as set difference
  Can be solved using O(#loss) memory
  Unique packet ID = <5-tuple, IP_Identification>
Mix all packets in the small memory at each switch
Collector subtracts two sets, same packets cancel out
Notes: First give an overview of the whole algoritm process
===
IP_ID: IP_identification
==
put all packet in a small memory
lost information

## Slide 14: Invertible Bloom Filter: multiple hashes
H1
xorSum count |  |  |  |  | 
a
H2
H3
[Invertible Bloom Filter (Sigcomm’ 11)]
a = <5-tuple, IP_Identification >

## Slide 15: Invertible Bloom Filter: multiple hashes
H1
xorSum count | a 1 |  | a 1 | a 1 | 
a
H2
H3
[Invertible Bloom Filter (Sigcomm’ 11)]
a = <5-tuple, IP_Identification >

## Slide 16: Invertible Bloom Filter: mix packets with XOR
H1
xorSum count | a 1 |  | a 1 | a 1 | 
H2
H3
[Invertible Bloom Filter (Sigcomm’ 11)]
b

## Slide 17: Invertible Bloom Filter: mix packets with XOR
H1
xorSum count | a 1 | b 1 | a⊕b 2 | a 1 | b 2
H2
H3
[Invertible Bloom Filter (Sigcomm’ 11)]
b

## Slide 18: Same hash functions across switches
xorSum count | 0 0 | 0 0 | 0 0 | 0 0 | 0 0
xorSum count | 0 0 | 0 0 | 0 0 | 0 0 | 0 0
upstream
downstream
Collector
[Invertible Bloom Filter (Sigcomm’ 11)]
Notes: How to set the size (accuracy, loss)
Add: variation of bloom filter, to help audience understand
===
Example, how we use it to achieve…
2 sw, UM at 1st sw, DM at 2nd sw. Each meter keeps an IBF
Each cell has two fields

## Slide 19: Same hash functions across switches
a
a
a
xorSum count | a 1 | 0 0 | a 1 | a 1 | 0 0
xorSum count | 0 0 | 0 0 | 0 0 | 0 0 | 0 0
upstream
downstream
Collector
a
drop
[Invertible Bloom Filter (Sigcomm’ 11)]
Notes: Pkt a comes, dropped, UM updated, DM doesn’t see it, so not updated. a = 5tuple + IPID, uniquely identify a pkt. Each pkt hashed to multiple cells, xor, count
Each element is hashed by the hash functions into multiple cells, and xors itself to the xorSum field, and increments the count field.

## Slide 20: Same hash functions across switches
b
b
b
xorSum count | a 1 | b 1 | a⊕b 2 | a 1 | b 1
xorSum count | 0 0 | b 1 | b 1 | 0 0 | b 1
a
a
a
upstream
downstream
Collector
b
b
b
b
b
[Invertible Bloom Filter (Sigcomm’ 11)]
Notes: Pkt b

## Slide 21: Same hash functions across switches
c
c
c
upstream
downstream
Collector
xorSum count | a⊕c 2 | b⊕c 2 | a⊕b 2 | a⊕c 2 | b 1
xorSum count | 0 0 | b 1 | b 1 | 0 0 | b 1
b
b
b
a
a
a
b
b
b
c
drop
[Invertible Bloom Filter (Sigcomm’ 11)]
Notes: Pkt c

## Slide 22: Same hash functions across switches
d
d
d
upstream
downstream
Collector
xorSum count | a⊕c⊕d 3 | b⊕c 2 | a⊕b⊕d 3 | a⊕c 2 | b⊕d 2
xorSum count | d 1 | b 1 | b⊕d 2 | 0 0 | b⊕d 2
c
c
c
b
b
b
a
a
a
b
b
b
d
d
d
d
d
xorSum count | a⊕c 2 | c 1 | a 1 | a⊕c 2 | 0 0
c
a
a
a
c
c
Collector does
subtraction
[Invertible Bloom Filter (Sigcomm’ 11)]
Notes: Important to note that
This is key to achieve
==
Pkt d
Fine to keep adding as many pkts as we have.
Collector receives both IBFs, subtraction, xorring up the xorSum of corresponding cells, subtract the cnt of 2nd IBF from the cnt of 1st IBF of the corresp…
Note, because pkts at both cancel out, only dropped pkts remain in the result. So memory usage is prop to #losses.
Look, this is very similar to what the counting table in FlowRadar did. Now we have no pure cells. But don’t worry, let’s see another set.

## Slide 23: Retrieve losses
xorSum count | a⊕c 2 | c 1 | a 1 | a⊕c 2 | 0 0
c
a
a
a
c
c
Collector
Notes: Control plane: how long to pull and calculate, mention it

## Slide 24: Retrieve losses
xorSum count | a⊕c 2 | c 1 | a 1 | a⊕c 2 | 0 0
c
a
a
a
c
c
Loss:
-1
-1
-1
c
Collector

## Slide 25: Retrieve losses
xorSum count | a 1 | 0 0 | a 1 | a 1 | 0 0
a
a
a
a
Loss:
c
-1
-1
-1
Collector
Only need O(#loss) memory
Notes: False positive, mention some number

## Slide 26: Benefits
Memory-efficient
Report a batch of packets every 10 ms
  ~10Mbps for 10Gbps traffic (including incast, blackhole and random drops)
Extend to collect more packet information
  TTL: help identify loops
  Timestamp
  Any other fields that programmable switches can configure
Easy to implement in P4
Notes: 1st: Memory efficient, prop… in ns3 simulation, use traffic ..., each meter only uses 10KB to support all losses per 10ms.
Also, extend …
The first benefit of our approach is that it is memory-efficient, because the memory usage is only proportional to the number of losses, not the total number of packets. Also, we can have many details of each individual loss. Remember that in the previous example, we xor the element into the first field. Here, the element can include any information of a packet, such as 5-tuple and IPID, which identifies each individual dropped packet, the TTL which helps identify loops, and timestamps. We need to tag the timestamp in the packet headers at the upstream, so that the downstream can get the same timestamp value to cancel out. We can configure to include any fields as it is easy to do so in programmable switches.

## Slide 27: Challenge: batch alignment
Ideally
In fact
upstream
downstream
Notes: we have showed that each switch send a batch of packet in the small memory every 10 ms. Ideally…

## Slide 28: Solution: packets carry batch ID
Just need 1 bit to distinguish adjacent batches
0
0
0
0
0
0
0
1
1
1
1
upstream
downstream
Notes: Make the speak concise
===
Mention the duration of downstraem batch
===
say there is no false positive

## Slide 29: Need to cover the whole network
meter
meter
meter
meter
meter
Notes: We have shown how to detect losses between two switches.

## Slide 30: Solution: pair-wise deployment
Cover all pipelines
UM
DM
UM
DM
Cover ingress pipeline
Cover egress pipeline
UM: Upstream meter
DM: Downstream meter
UM
DM
UM
DM
Ingress pipeline
shared
buffer
Egress pipeline
DM
UM
DM
UM
Notes: Add: Multiple small meters instead of one big meter
Emphasize on the meter order in a switch
===
Example
loss within switch, e.g. table
-> cover all pipelines
ingress pipeline: UM at previous hop, DM at this hop
egress pipeline: UM at this hop, DM at next hop
UM before DM: every part is coverd.

## Slide 31: Challenge: incremental deployment
Compare sum(UMi) and sum(DMi)
Blackbox
UM
DM
UM
DM
LossRadar
LossRadar
UM
DM
LossRadar
LossRadar
UM
DM

## Slide 32: LossRadar overview
Fast detection
Knowing location
Include details of each loss
Being generic
Low overhead
Digest Collector
Traffic Digest
Traffic Digest
Traffic Digest

## Slide 33: Root cause inference
Digest Collector
Traffic Digest
Traffic Digest
Traffic Digest
Root cause inference
Notes: now we have all the details
highlight the details

## Slide 34: Root cause inference
Different root causes have different loss patterns
  Temporal: how the losses distribute over time
  Inter-flow: specific set of flows? All flows?
  Intra-flow: which packets of a flow?

## Slide 35: Root cause inference
Different root causes have different loss patterns
  Temporal: how the losses distribute over time
  Inter-flow: specific set of flows? All flows?
  Intra-flow: which packets of a flow?
Chart: Time (us)
| 1.0 | 2.0 | 3.0 | 4.0 | 5.0 | 6.0 | 7.0 | 8.0 | 9.0 | 10.0 | 11.0 | 12.0 | 13.0 | 14.0 | 15.0 | 16.0 | 17.0 | 18.0 | 19.0 | 20.0 | 21.0 | 22.0 | 23.0 | 24.0 | 25.0 | 26.0 | 27.0 | 28.0 | 29.0 | 30.0
Y-Value 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 1 | 0 | 0 | 1 | 0 | 1 | 1 | 0 | 1 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Chart: Time (us)
| 1.0 | 2.0 | 3.0 | 4.0 | 5.0 | 6.0 | 7.0 | 8.0 | 9.0 | 10.0 | 11.0 | 12.0 | 13.0 | 14.0 | 15.0 | 16.0 | 17.0 | 18.0 | 19.0 | 20.0 | 21.0 | 22.0 | 23.0 | 24.0 | 25.0 | 26.0 | 27.0 | 28.0 | 29.0 | 30.0
Y-Value 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1
Chart: Time (us)
| 1.0 | 2.0 | 3.0 | 4.0 | 5.0 | 6.0 | 7.0 | 8.0 | 9.0 | 10.0 | 11.0 | 12.0 | 13.0 | 14.0 | 15.0 | 16.0 | 17.0 | 18.0 | 19.0 | 20.0 | 21.0 | 22.0 | 23.0 | 24.0 | 25.0 | 26.0 | 27.0 | 28.0 | 29.0 | 30.0
Y-Value 1 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 1 | 1
Dst IP = 10.0.0.0/24

## Slide 36: Root cause inference
Different root causes have different loss patterns
  Temporal: how the losses distribute over time
  Inter-flow: specific set of flows? All flows?
  Intra-flow: which packets of a flow?
 | Temporal | Inter-flow | Intra-flow
Congestion | Bursty | All flows on an egress port | Non-deterministic
Blackhole | Bursty / non-bursty | Specific flows | Consecutive
Random drops | Non-bursty | All flows | Non-deterministic
LossRadar
Timestamp
5-tuple
IP_ID
 | Temporal | Inter-flow | Intra-flow
Congestion | Bursty | All flows on an egress port | Non-deterministic
Blackhole | Bursty / non-bursty | Specific flows | Consecutive
 | Temporal | Inter-flow | Intra-flow
Congestion | Bursty | All flows on an egress port | Non-deterministic
Notes: Mention the duration of the controller calculation (from detection to inference)
===
also slightly mentions other types : congestion
add figures from challenge
==
Define the three dimensions.
Intra-flow –> consecutiveness
Say one example problem, how the 3 dimention distinguish it.

## Slide 37: LossRadar evaluation
Simulation of k=8 FatTree in ns3
  80 switches, 128 hosts, 10G links
Send traffic according to the pattern in DCTCP
Inject different types of losses
  Incast
  Blackholes
  random drops
Each switch reports the traffic digest every 10 ms.
Notes: Relate to the different types motivation
Add problems to diff types
===
start with topology
[solved] query is a way to inject loss

## Slide 38: Low memory usage
Notes: Emphsize the large traffic (not the incast #)
may use popups
===
Y values wrong
Add slide for comparison with other systems
==
When loss rate is 0.1%
Only 0.5% bandwidth compared to NetSight
And 1.4% memory compared to FlowRadar
===
[solved] remove batch curves
comparison with previous works: say numbers

## Slide 39: Compare with state-of-the-art solutions
LossRadar vs. full mirroring
  0.5% bandwidth compared to NetSight with batch compression
LossRadar vs. per-flow counter
  1.4% memory compared to FlowRadar

## Slide 40: High inference accuracy across all types
Notes: Takeaway: For case not identified, because mix, and very hard to distinguish, even by human
===
Close to 100% precision means low false positive
Moreover, correctly identify the root cause behind the losses

## Slide 41: Conclusion
Loss diagnosis is very important
  High impact on performance
  Diagnosis takes a lot of human effort
LossRadar can detect losses and diagnose root causes
  Detection: details of individual losses, with locations, within 10ms
  Diagnosis: correctly discover root causes
P4 code: https://github.com/liyuliang001/LossRadar-P4
Notes: ===
start with: loss is important
goal : detect + inference
sub-detect: build a tool: capture ...
all properties
sub-inference
all types
fast detection (10ms)

## Slide 42: Existing tools fall short
SNMP counter: Not generic to all types, slow
Flow-level counter [NetFlow, FlowRadar]: No details of individual packets
Host monitoring [Trumpet, Pingmesh]: Don’t know location
Mirroring [NetSight, Everflow]: Too much overhead
Notes: Cut this slide, move to backup
===
List some papers: control plane (sherlock)
[solved] Add paper names
==
Explain each one
SNMP also slow
cannot have one counter for each type
for major one, counter is helpful,
but for all, not a good direction to add counter for each